## Slide 1: Instruction set of 8086

## Slide 2: The Instruction set of 8086:-
Data transfer instructions
Arithmetic instructions
Logical Instructions

## Slide 3: Data transfer instructions
General purpose instructions:
MOV − Used to copy the byte or word from the provided source to the provided destination.
-syntax- MOV destination,source
Ex:-MOV AX,BX; contents of bx moved to ax.
PUSH − Used to put a word at the top of the stack.
Ex:-push AX; contents Ax reg moved to the stack.
POP − Used to get a word from the top of the stack to the provided location.
Eg:-pop Ax; contents from top of stack moved to AX.
XCHG − Used to exchange the data from two locations.
Eg:-XCHG ax,bx

## Slide 4: Data transfer instructions..contd
B. Instructions for input and output port transfer
  IN − Used to read a byte or word from the provided port to the accumulator(AX register).
  OUT − Used to send out a byte or word from the accumulator to the provided port.
C. Instructions to transfer the address
  LEA − Used to load the address of operand into the provided register.
  LDS − Used to load DS register from the memory
  LES − Used to load ES register from the memory.

## Slide 5: Data transfer instructions..contd
D. Instructions to transfer flag registers
LAHF − Used to load AH with the low byte of the flag register.
SAHF − Used to store AH register to low byte of the flag register.
PUSHF − Used to copy the flag register at the top of the stack.
POPF − Used to copy a word at the top of the stack to the flag register.

## Slide 6: Instruction :POP Destination
This instruction copies a word from memory location pointed by SS:SP to the destination.
The segment register used with SP is SS , and no segment override is possible.
When it is executed:
    Data from memory location (in stack segment) SS:SP is first copied to the destination
    And then SP is incremented by 2 (SP=SP+2)
    Note : destination can be a general purpose register, Flag register ,segment register or memory location .
    EX: POP AX
    POP DS

## Slide 7: Instruction :PUSH Source
When this instruction is executed:
SP=SP-2 (i.e. First SP is decremented by 2 )
Copy the word from source register to the location in Stack Segment where SP points.
Note :1.Source operand (16-bit) can be a general purpose register, Flag register ,segment register or memory .
EX: PUSH AX
PUSH BX
PUSH DS

## Slide 8: XCHG
XCHG Reg2,Reg1
Contents of Reg2 are exchanged with Reg1.
Both Reg’s should be of same size.
Both can be ether 8 bit or 16 bit.
Eg:-XCHG AL,BL
XCHG [BX],AX

## Slide 9: ARITHMETIC INSTRUCTIONS 1.instructions to perform addition

## Slide 10: ADDITION instructions..cntd
ADD
Ex ADD AX,BX
AX<= AX+BX
ADC
Ex ADD AX,BX
AX<= AX+BX+CF
INC
Ex: INC CL
CL<= CL+1
INC BX
BX<= BX+1
AAA
DAA

## Slide 11: 2.Instructions to perform subtraction

## Slide 12: SUBTRACT INSTRUCTIONS
1.SUB
Eg:-SUB ax, bx ; Subtracts bx from ax and stores result in ax.
2.SBB ax,bx ; Subtracts bx and borrow(carry flag) from ax and stores result in ax.
3.CMP ax,bx ; comparison is done by subtracting bx from ax and checking the flags.
-If ax<bx –carry flag set
-ax=bx, zero flag set

## Slide 13: SUBTRACT INSTRUCTIONS
4.dec
Eg: DEC ax- Decrements the value of ax by 1.

## Slide 14: 3.Instruction to perform Multiplication

## Slide 15: MULTIPLICATION
Eg:-1.Mul bl
Multiplies AL by BL and stores the result in AL.
2.Mul bx
Multiplies ax with bx and stores the stores the lower bytes of the result in Ax and higher bytes in DX.

## Slide 16: 4.Instrutions for Division

## Slide 17: DIVISION
Eg:-Div BL
-AL is divided by BL and the quotient is stored in AL and the reminder in AH register.
Eg:-Div BX
-Ax is divided by BX and the Quotient is stored in AX and the reminder in DX.

## Slide 18: Logical Instructions